## Slide 1: Chapter 4
The Processor

## Slide 2: Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two RISC-V implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or
  Control transfer: beq
§4.1 Introduction

## Slide 3: Instruction Execution
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 4: CPU Overview

## Slide 5: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 6: Control

## Slide 7: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 8: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 9: Sequential Elements
Register: stores data in a circuit
  Uses a clock signal to determine when to update the stored value
  Edge-triggered: update when Clk changes from 0 to 1
D
Clk
Q
Clk
D
Q

## Slide 10: Sequential Elements
Register with write control
  Only updates on clock edge when write control input is 1
  Used when stored value is required later
D
Clk
Q
Write
Write
D
Q
Clk

## Slide 11: Clocking Methodology
Combinational logic transforms data during clock cycles
  Between clock edges
  Input from state elements, output to state element
  Longest delay determines clock period

## Slide 12: Building a Datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a RISC-V datapath incrementally
  Refining the overview design
§4.3 Building a Datapath

## Slide 13: Instruction Fetch
64-bit register
Increment by 4 for next instruction

## Slide 14: R-Format Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 15: Load/Store Instructions
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Load: Read memory and update register
Store: Write register value to memory

## Slide 16: Branch Instructions
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value

## Slide 17: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 18: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 19: R-Type/Load/Store Datapath

## Slide 20: Full Datapath

## Slide 21: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on opcode
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract

## Slide 22: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | Opcode field | ALU function | ALU control
ld | 00 | load register | XXXXXXXXXXX | add | 0010
sd | 00 | store register | XXXXXXXXXXX | add | 0010
beq | 01 | branch on equal | XXXXXXXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001

## Slide 23: The Main Control Unit
Control signals derived from instruction

## Slide 24: Datapath With Control

## Slide 25: R-Type Instruction

## Slide 26: Load Instruction

## Slide 27: BEQ Instruction

## Slide 28: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Not feasible to vary period for different instructions
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 29: Pipelining Analogy
Pipelined laundry: overlapping execution
  Parallelism improves performance
§4.5 An Overview of Pipelining
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/0.5n + 1.5 ≈ 4 = number of stages

## Slide 30: RISC-V Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 31: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 32: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 33: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease

## Slide 34: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage

## Slide 35: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 36: Structure Hazards
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 37: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add x19, x0, x1 sub x2, x19, x3

## Slide 38: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 39: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 40: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for a = b + e; c = b + f;
ld x1, 0(x0)
ld x2, 8(x0)
add x3, x1, x2
sd x3, 24(x0)
ld x4, 16(x0)
add x5, x1, x4
sd x5, 32(x0)
stall
stall
ld x1, 0(x0)
ld x2, 8(x0)
ld x4, 16(x0)
add x3, x1, x2
sd x3, 24(x0)
add x5, x1, x4
sd x5, 32(x0)
11 cycles
13 cycles

## Slide 41: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 42: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 43: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In RISC-V pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 44: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 45: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 46: RISC-V Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 47: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 48: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 49: IF for Load, Store, …

## Slide 50: ID for Load, Store, …

## Slide 51: EX for Load

## Slide 52: MEM for Load

## Slide 53: WB for Load
Wrong register number

## Slide 54: Corrected Datapath for Load

## Slide 55: EX for Store

## Slide 56: MEM for Store

## Slide 57: WB for Store

## Slide 58: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 59: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 60: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 61: Pipelined Control (Simplified)

## Slide 62: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 63: Pipelined Control

## Slide 64: Data Hazards in ALU Instructions
Consider this sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 65: Dependencies & Forwarding

## Slide 66: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 67: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 68: Forwarding Paths

## Slide 69: Forwarding Conditions
Mux control | Source | Explanation
ForwardA = 00 | ID/EX | The first ALU operand comes from the register file.
ForwardA = 10 | EX/MEM | The first ALU operand is forwarded from the prior ALU result.
ForwardA = 01 | MEM/WB | The first ALU operand is forwarded from data memory or an earlier ALU result.
ForwardB = 00 | ID/EX | The second ALU operand comes from the register file.
ForwardB = 10 | EX/MEM | The second ALU operand is forwarded from the prior ALU result.
ForwardB = 01 | MEM/WB | The second ALU operand is forwarded from data memory or an earlier ALU result.

## Slide 70: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 71: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRs2))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 72: Datapath with Forwarding

## Slide 73: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs2))
If detected, stall and insert bubble

## Slide 74: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 75: Load-Use Data Hazard
Stall inserted here

## Slide 76: Datapath with Hazard Detection

## Slide 77: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 78: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 79: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub x10, x4, x8 40: beq x1, x3, 16 // PC-relative branch // to 40+16*2=72 44: and x12, x2, x5 48: orr x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)

## Slide 80: Example: Branch Taken

## Slide 81: Example: Branch Taken

## Slide 82: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 83: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 84: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 85: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 86: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard
§4.9 Exceptions

## Slide 87: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 0000 0000 1C09 0000hex

## Slide 88: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
  …: …
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 89: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use SEPC to return to program
Otherwise
  Terminate program
  Report error using SEPC, SCAUSE, …

## Slide 90: Exceptions in a Pipeline
Another form of control hazard
Consider malfunction on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set SEPC and SCAUSE register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 91: Pipeline with Exceptions

## Slide 92: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in SEPC register
  Identifies causing instruction

## Slide 93: Exception Example
Exception on add in
  40 sub x11, x2, x4 44 and x12, x2, x5 48 orr x13, x2, x6 4c add x1, x2, x1 50 sub x15, x6, x7 54 ld x16, 100(x7) …
Handler
  1C090000 sd x26, 1000(x10) 1c090004 sd x27, 1008(x10) …

## Slide 94: Exception Example

## Slide 95: Exception Example

## Slide 96: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 97: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 98: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions

## Slide 99: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 100: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 101: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 102: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 103: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 104: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 105: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 106: RISC-V with Static Dual Issue

## Slide 107: Hazards in the Dual-Issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x10, x0, x1 ld x2, 0(x10)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 108: Scheduling Example
Schedule this for dual-issue RISC-V
Loop: ld x31,0(x20) // x31=array element add x31,x31,x21 // add scalar in x21 sd x31,0(x20) // store result addi x20,x20,-8 // decrement pointer blt x22,x20,Loop // branch if x22 < x20
 | ALU/branch | Load/store | cycle
Loop: | nop | ld x31,0(x20) | 1
 | addi x20,x20,-8 | nop | 2
 | add x31,x31,x21 | nop | 3
 | blt x22,x20,Loop | sd x31,8(x20) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 109: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 110: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi x20,x20,-32 | ld x28, 0(x20) | 1
 | nop | ld x29, 24(x20) | 2
 | add x28,x28,x21 | ld x30, 16(x20) | 3
 | add x29,x29,x21 | ld x31, 8(x20) | 4
 | add x30,x30,x21 | sd x28, 32(x20) | 5
 | add x31,x31,x21 | sd x29, 24(x20) | 6
 | nop | sd x30, 16(x20) | 7
 | blt x22,x20,Loop | sd x31, 8(x20) | 8

## Slide 111: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 112: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
  Can start sub while add is waiting for ld

## Slide 113: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 114: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 115: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 116: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 117: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 118: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 119: Cortex A53 and Intel i7
Processor | ARM A53 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 100 milliWatts (1 core @ 1 GHz) | 130 Watts
Clock rate | 1.5 GHz | 2.66 GHz
Cores/Chip | 4 (configurable) | 4
Floating point? | Yes | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 8 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | Hybrid | 2-level
1st level caches/core | 16-64 KiB I, 16-64 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-2048 KiB | 256 KiB (per core)
3rd level caches (shared) | (platform dependent) | 2-8 MB
§4.11 Real Stuff: The ARM Cortex-A53 and Intel Core i7 Pipelines

## Slide 120: ARM Cortex-A53 Pipeline

## Slide 121: ARM Cortex-A53 Performance

## Slide 122: Core i7 Pipeline

## Slide 123: Core i7 Performance

## Slide 124: Matrix Multiply
Unrolled C code
1 #include <x86intrin.h>
2 #define UNROLL (4)
3
4 void dgemm (int n, double* A, double* B, double* C)
5 {
6 for ( int i = 0; i < n; i+=UNROLL*4 )
7 for ( int j = 0; j < n; j++ ) {
8 __m256d c[4];
9 for ( int x = 0; x < UNROLL; x++ )
10 c[x] = _mm256_load_pd(C+i+x*4+j*n);
11
12 for( int k = 0; k < n; k++ )
13 {
14 __m256d b = _mm256_broadcast_sd(B+k+j*n);
15 for (int x = 0; x < UNROLL; x++)
16 c[x] = _mm256_add_pd(c[x],
17 _mm256_mul_pd(_mm256_load_pd(A+n*k+x*4+i), b));
18 }
19
20 for ( int x = 0; x < UNROLL; x++ )
21 _mm256_store_pd(C+i+x*4+j*n, c[x]);
22 }
23 }
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 125: Matrix Multiply
Assembly code:
1 vmovapd (%r11),%ymm4 # Load 4 elements of C into %ymm4
2 mov %rbx,%rax # register %rax = %rbx
3 xor %ecx,%ecx # register %ecx = 0
4 vmovapd 0x20(%r11),%ymm3 # Load 4 elements of C into %ymm3
5 vmovapd 0x40(%r11),%ymm2 # Load 4 elements of C into %ymm2
6 vmovapd 0x60(%r11),%ymm1 # Load 4 elements of C into %ymm1
7 vbroadcastsd (%rcx,%r9,1),%ymm0 # Make 4 copies of B element
8 add $0x8,%rcx # register %rcx = %rcx + 8
9 vmulpd (%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
10 vaddpd %ymm5,%ymm4,%ymm4 # Parallel add %ymm5, %ymm4
11 vmulpd 0x20(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
12 vaddpd %ymm5,%ymm3,%ymm3 # Parallel add %ymm5, %ymm3
13 vmulpd 0x40(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
14 vmulpd 0x60(%rax),%ymm0,%ymm0 # Parallel mul %ymm1,4 A elements
15 add %r8,%rax # register %rax = %rax + %r8
16 cmp %r10,%rcx # compare %r8 to %rax
17 vaddpd %ymm5,%ymm2,%ymm2 # Parallel add %ymm5, %ymm2
18 vaddpd %ymm0,%ymm1,%ymm1 # Parallel add %ymm0, %ymm1
19 jne 68 <dgemm+0x68> # jump if not %r8 != %rax
20 add $0x1,%esi # register % esi = % esi + 1
21 vmovapd %ymm4,(%r11) # Store %ymm4 into 4 C elements
22 vmovapd %ymm3,0x20(%r11) # Store %ymm3 into 4 C elements
23 vmovapd %ymm2,0x40(%r11) # Store %ymm2 into 4 C elements
24 vmovapd %ymm1,0x60(%r11) # Store %ymm1 into 4 C elements

## Slide 126: Performance Impact

## Slide 127: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls

## Slide 128: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 129: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks